## Slide 1: Electronics Overview
Basic Circuits, Power Supplies,
Transistors, Cable Impedance
diode bridge

## Slide 2: Basic Circuit Analysis
What we won’t do:
  common electronics-class things: RLC, filters, detailed analysis
What we will do:
  set out basic relations
  look at a few examples of fundamental importance (mostly resistive circuits)
  look at diodes, voltage regulation, transistors
  discuss impedances (cable, output, etc.)

## Slide 3: The Basic Relations
V is voltage (volts: V); I is current (amps: A); R is resistance (ohms: ); C is capacitance (farads: F); L is inductance (henrys: H)
Ohm’s Law: V = IR; V = ; V = L(dI/dt)
Power: P = IV = V2/R = I2R
Resistors and inductors in series add
Capacitors in parallel add
Resistors and inductors in parallel, and capacitors in series add according to:

## Slide 4: Example: Voltage divider
Voltage dividers are a classic way to set a voltage
Works on the principle that all charge flowing through the first resistor goes through the second
  so V  R-value
  provided any load at output is negligible: otherwise some current goes there too
So Vout = V(R2/(R1 + R2))
R2 here is a variable resistor, or potentiometer, or “pot”
  typically three terminals: R12 is fixed, tap slides along to vary R13 and R23, though R13 + R23 = R12 always
1
2
3
R1
R2
V
Vout

## Slide 5: Real Batteries: Output Impedance
A power supply (battery) is characterized by a voltage (V) and an output impedance (R)
  sometimes called source impedance
Hooking up to load: Rload, we form a voltage divider, so that the voltage applied by the battery terminal is actually Vout = V(Rload/(R+Rload))
  thus the smaller R is, the “stiffer” the power supply
  when Vout sags with higher load current, we call this “droop”
Example: If 10.0 V power supply droops by 1% (0.1 V) when loaded to 1 Amp (10  load):
  internal resistance is 0.1 
  called output impedance or source impedance
  may vary with load, though (not a real resistor)
V
R
D-cell example: 6A
out of 1.5 V battery
indicates 0.25  output
impedance

## Slide 6: Power Supplies and Regulation
A power supply typically starts with a transformer
  to knock down the 340 V peak-to-peak (120 V AC) to something reasonable/manageable
We will be using a center-tap transformer
  (A’  B’) = (winding ratio)(A  B)
    when A > B, so is A’ > B’
  geometry of center tap (CT) guarantees it is midway between A’ and B’ (frequently tie this to ground so that A’ = B’)
  note that secondary side floats: no ground reference built-in
A
B
A’
CT
B’
AC input
AC output

## Slide 7: Diodes
Diodes are essentially one-way current gates
Symbolized by:
Current vs. voltage graphs:
V
I
V
I
V
I
V
I
0.6 V
plain resistor
diode
idealized diode
WAY idealized diode
no current flows
current flows
the direction the
arrow points in the
diode symbol is the
direction that current
will flow
acts just like a wire
(will support arbitrary
current) provided that
voltage is positive

## Slide 8: Diode Makeup
Diodes are made of semiconductors (usually silicon)
Essentially a stack of p-doped and n-doped silicon to form a p-n junction
  doping means deliberate impurities that contribute extra electrons (n-doped) or “holes” for electrons (p-doped)
Transistors are n-p-n or p-n-p arrangements of semiconductors
p-type
n-type

## Slide 9: LEDs: Light-Emitting Diodes
Main difference is material is more exotic than silicon used in ordinary diodes/transistors
  typically 2-volt drop instead of 0.6 V drop
When electron flows through LED, loses energy by emitting a photon of light rather than vibrating lattice (heat)
LED efficiency is 30% (compare to incandescent bulb at 10%)
Must supply current-limiting resistor in series:
  figure on 2 V drop across LED; aim for 1–10 mA of current

## Slide 10: Getting DC back out of AC
AC provides a means for us to distribute electrical power, but most devices actually want DC
  bulbs, toasters, heaters, fans don’t care: plug straight in
  sophisticated devices care because they have diodes and transistors that require a certain polarity
    rather than oscillating polarity derived from AC
    this is why battery orientation matters in most electronics
Use diodes to “rectify” AC signal
Simplest (half-wave) rectifier uses one diode:
AC source
load
input voltage
voltage seen by load
diode only conducts
when input voltage is positive

## Slide 11: Doing Better: Full-wave Diode Bridge
The diode in the rectifying circuit simply prevented the negative swing of voltage from conducting
  but this wastes half the available cycle
  also very irregular (bumpy): far from a “good” DC source
By using four diodes, you can recover the negative swing:
A
C
B
D
AC source
load
input voltage
voltage seen by load
B & C conduct
A & D conduct

## Slide 12: Full-Wave Dual-Supply
By grounding the center tap, we have two opposite AC sources
  the diode bridge now presents + and  voltages relative to ground
  each can be separately smoothed/regulated
  cutting out diodes A and D makes a half-wave rectifier
A
C
B
D
AC source
+ load
 load
voltages seen by loads
can buy pre-packaged diode bridges

## Slide 13: Smoothing out the Bumps
Still a bumpy ride, but we can smooth this out with a capacitor
  capacitors have capacity for storing charge
  acts like a reservoir to supply current during low spots
  voltage regulator smoothes out remaining ripple
A
C
B
D
AC source
load
capacitor

## Slide 14: How smooth is smooth?
An RC circuit has a time constant  = RC
  because dV/dt = I/C, and I = V/R  dV/dt = V/RC
  so V is V0exp(t/)
Any exponential function starts out with slope = Amplitude/
So if you want < 10% ripple over 120 Hz (8.3 ms) timescale…
  must have  = RC > 83 ms
  if R = 100 , C > 830 F
R
C
V


## Slide 15: Regulating the Voltage
The unregulated, ripply voltage may not be at the value you want
  depends on transformer, etc.
  suppose you want 15.0 V
You could use a voltage divider to set the voltage
But it would droop under load
  output impedance  R1 || R2
  need to have very small R1, R2 to make “stiff”
  the divider will draw a lot of current
  perhaps straining the source
  power expended in divider >> power in load
Not a “real” solution
Important note: a “big load” means a small resistor value: 1  demands more current than 1 M
1
2
3
R1
R2
Vin
Vout
Rload

## Slide 16: The Zener Regulator
Zener diodes break down at some reverse voltage
  can buy at specific breakdown voltages
  as long as some current goes through zener, it’ll work
  good for rough regulation
Conditions for working:
  let’s maintain some minimal current, Iz through zener (say a few mA)
  then (Vin  Vout)/R1 = Iz + Vout/Rload sets the requirement on R1
  because presumably all else is known
  if load current increases too much, zener shuts off (node drops below breakdown) and you just have a voltage divider with the load
R1
Z
Vin
Vout = Vz
Rload
zener voltage
high slope is what makes the
zener a decent voltage regulator

## Slide 17: Voltage Regulator IC
Can trim down ripply voltage to precise, rock-steady value
Now things get complicated!
  We are now in the realm of integrated circuits (ICs)
ICs are whole circuits in small packages
ICs contain resistors, capacitors, diodes, transistors, etc.
note zeners

## Slide 18: Voltage Regulators
The most common voltage regulators are the LM78XX (+ voltages) and LM79XX ( voltages)
  XX represents the voltage
    7815 is +15; 7915 is 15; 7805 is +5, etc
  typically needs input > 3 volts above output (reg.) voltage
A versatile regulator is the LM317 (+) or LM337 ()
  1.2–37 V output
  Vout = 1.25(1+R2/R1) + IadjR2
  Up to 1.5 A
  picture at right can go to 25 V
  datasheetcatalog.com for details
beware that housing is not always ground

## Slide 19: Transistors
Transistors are versatile, highly non-linear devices
Two frequent modes of operation:
  amplifiers/buffers
  switches
Two main flavors:
  npn (more common) or pnp, describing doping structure
Also many varieties:
  bipolar junction transistors (BJTs) such as npn, pnp
  field effect transistors (FETs): n-channel and p-channel
  metal-oxide-semiconductor FETs (MOSFETs)
We’ll just hit the essentials of the BJT here
  MOSFET in later lecture
B
C
E
B
E
C
npn
pnp

## Slide 20: BJT Amplifier Mode
Central idea is that when in the right regime, the BJT collector-emitter current is proportional to the base current:
  namely, Ice = Ib, where  (sometimes hfe) is typically ~100
  In this regime, the base-emitter voltage is ~0.6 V
  below, Ib = (Vin  0.6)/Rb; Ice = Ib = (Vin  0.6)/Rb
  so that Vout = Vcc  IceRc = Vcc  (Vin  0.6)(Rc/Rb)
  ignoring DC biases, wiggles on Vin become  (Rc/Rb) bigger (and inverted): thus amplified
out
Rc
Rb
in
Vcc
B
C
E

## Slide 21: Switching: Driving to Saturation
What would happen if the base current is so big that the collector current got so big that the voltage drop across Rc wants to exceed Vcc?
  we call this saturated: Vc  Ve cannot dip below ~0.2 V
  even if Ib is increased, Ic won’t budge any more
The example below is a good logic inverter
  if Vcc = 5 V; Rc = 1 k; Ic(sat)  5 mA; need Ib > 0.05 mA
  so Rb < 20 k would put us safely into saturation if Vin = 5V
  now 5 V in  ~0.2 V out; < 0.6 V in  5 V out
out
Rc
Rb
in
Vcc

## Slide 22: Transistor Buffer
In the hookup above (emitter follower), Vout = Vin  0.6
  sounds useless, right?
  there is no voltage “gain,” but there is current gain
  Imagine we wiggle Vin by V: Vout wiggles by the same V
  so the transistor current changes by Ie = V/R
  but the base current changes 1/ times this (much less)
  so the “wiggler” thinks the load is V/Ib = ·V/Ie = R
  the load therefore is less formidable
The “buffer” is a way to drive a load without the driver feeling the pain (as much): it’s impedance isolation
out
R
in
Vcc

## Slide 23: Improved Zener Regulator
By adding a transistor to the zener regulator from before, we no longer have to worry as much about the current being pulled away from the zener to the load
  the base current is small
  Rload effectively looks  times bigger
  real current supplied through transistor
Can often find zeners at 5.6 V, 9.6 V, 12.6 V, 15.6 V, etc. because drop from base to emitter is about 0.6 V
  so transistor-buffered Vreg comes out to 5.0, 9.0, etc.
Iz varies less in this arrangement, so the regulated voltage is steadier
Vreg
Rload
Vz
Vin
Rz
Z
Vin

## Slide 24: Switching Power Supplies
Power supplies without transformers
  lightweight; low cost
  can be electromagnetically noisy
Use a DC-to-DC conversion process that relies on flipping a switch on and off, storing energy in an inductor and capacitor
  regulators were DC-to-DC converters too, but lossy: lose P = IV of power for voltage drop of V at current I
  regulators only down-convert, but switchers can also up-convert
  switchers are reasonably efficient at conversion

## Slide 25: Switcher topologies
from: http://www.maxim-ic.com/appnotes.cfm/appnote_number/4087
The FET switch is turned off or on in a pulse-width-modulation (PWM) scheme,
the duty cycle of which determines the ratio of Vout to Vin

## Slide 26: Step-Down Calculations
If the FET is on for duty cycle, D (fraction of time on), and the period is T:
  the average output voltage is Vout = DVin
  the average current through the capacitor is zero, the average current through the load (and inductor) is 1/D times the input current
  under these idealizations, power in = power out

## Slide 27: Step-down waveforms
Shown here is an example of the step-down with the FET duty cycle around 75%
The average inductor current (dashed) is the current delivered to the load
  the balance goes to the capacitor
The ripple (parabolic sections) has peak-to-peak fractional amplitude of T2(1D)/(8LC)
  so win by small T, large L & C
  10 kHz at 1 mH, 1000 F yields ~0.1% ripple
  means 10 mV on 10 V
FET
Inductor
Current
Supply
Current
Capacitor
Current
Output
Voltage
(ripple exag.)

## Slide 28: Cable Impedances
RG58 cable is characterized as 50  cable
  RG59 is 75 
  some antenna cable is 300 
Isn’t the cable nearly zero resistance? And shouldn’t the length come into play, somehow?
There is a distinction between resistance and impedance
  though same units
Impedances can be real, imaginary, or complex
  resistors are real: Z = R
  capacitors and inductors are imaginary: Z = i/C; Z = iL
  mixtures are complex: Z = R  i/C + iL

## Slide 29: Impedances, cont.
Note that:
  capacitors become less “resistive” at high frequency
  inductors become more “resistive” at high frequency
  bigger capacitors are more transparent
  bigger inductors are less transparent
  i (√1) indicates 90 phase shift between voltage and current
    after all, V = IZ, so Z = V/I
    thus if V is sine wave, I is cosine for inductor/capacitor
    and given that one is derivative, one is integral, this makes sense (slide # 3)
  adding impedances automatically takes care of summation rules: add Z in series
    capacitance adds as inverse, resistors, inductors straight-up

## Slide 30: Impedance Phasor Diagram
Impedances can be drawn on a complex plane, with pure resistive, inductive, and capacitive impedances represented by the three cardinal arrows
An arbitrary combination of components may have a complex impedance, which can be broken into real and imaginary parts
Note that a system’s impedance is frequency-dependent
R
L
Z
Zr
Zi
1/C
real axis
imag. axis

## Slide 31: Transmission Line Model
The cable has a finite capacitance per unit length
  property of geometry and dielectric separating conductors
  C/l = 2πε/ln(b/a), where b and a are radii of cylinders
Also has an inductance per unit length
  L/l = (μ/2π)ln(b/a)
When a voltage is applied, capacitors charge up
  thus draw current; propagates down the line near speed of light
Question: what is the ratio of voltage to current?
  because this is the characteristic impedance
Answer: Z0 = sqrt(L/C) = sqrt(L/C) = (1/2π)sqrt(μ/ε)ln(b/a)
  note that Z0 is frequency-independent
C
L
input
output

## Slide 32: Typical Transmission Lines
RG58 coax is abundant
  30 pF per foot; 75 nH per foot; 50 ; v = 0.695c; ~5 ns/m
RG174 is the thin version
  same parameters as above, but scaled-down geometry
RG59
  used for video, cable TV
  21 pF/ft; 118 nH per foot; 75 ; v = 0.695c; ~5 ns/m
twisted pair
  110  at 30 turns/ft, AWG 24–28
PCB (PC-board) trace
  get 50  if the trace width is 1.84 times the separation from the ground plane (assuming fiberglass PCB with  = 4.5)

## Slide 33: Why impedance matters
For fast signals, get bounces (reflections) at every impedance mismatch
  reflection amplitude is (Zt  Zs)/(Zt + Zs)
    s and t subscripts represent source and termination impedances
    sources intending to drive a Z0 cable have Zs = Z0
Consider a long cable shorted at end: insert pulse
  driving electronics can’t know about the termination immediately: must charge up cable as the pulse propagates forward, looking like Z0 of the cable at first
  surprise at far end: it’s a short! retreat!
  in effect, negative pulse propagates back, nulling out capacitors (reflection is 1)
  one round-trip later (10 ns per meter, typically), the driving electronics feels the pain of the short

## Slide 34: Impedance matters, continued
Now other extreme: cable un-terminated: open
  pulse travels merrily along at first, the driving electronics seeing a Z0 cable load
  at the end, the current has nowhere to go, but driver can’t know this yet, so keeps loading cable as if it’s still Z0
  effectively, a positive pulse reflects back, double-charging capacitors (reflection is +1)
  driver gets word of this one round-trip later (10 ns/m, typically), then must cease to deliver current (cable fully charged)
The goldilocks case (reflection = 0)
  if the end of the cable is terminated with resistor with R = Z0, then current is slurped up perfectly with no reflections
  the driver is not being lied to, and hears no complaints

## Slide 35: So Beware!
If looking at fast (tens of ns domain) signals on scope, be sure to route signal to scope via 50  coax and terminate the scope in 50 
  if the signal can’t drive 50 , then use active probes
Note that scope probes terminate to 1 M, even though the cables are NOT 1 M cables (no such thing)
  so scope probes can be very misleading about shapes of fast signals

## Slide 36: References and Assignment
References:
  The canonical electronics reference is Horowitz and Hill: The Art of Electronics
  Also the accompanying lab manual by Hayes and Horowitz is highly valuable (far more practically-oriented)
  And of course: Electronics for Dogs (just ask Gromit)
Reading
  Sections 6.1.1, 6.1.2
  Skim 6.2.2, 6.2.3, 6.2.4
  Sections 6.3.1, 6.5.1, 6.5.2
  Skim 6.3.2